## Slide 1
FINAL PROJECT PRESENTATION | 2026–27
LSTM Autoencoder-Based Persistent and Transient Anomaly Classification in Open RAN KPIs
Machine Learning • Open Radio Access Networks
Yaswanth Srikar | 2520040026 Omprakash Jena | 2520040057 Rishi Vardhan | 2520040078
Guide: Dr. Vinnakota Venu Balaji • Department of ECE

## Slide 2
01 • INTRODUCTION
The problem: not every anomaly is a fault
Open RAN produces time-dependent KPIs that need context, not just fixed thresholds.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
2
NORMAL
KPIs follow expected patterns.
TRANSIENT
A short deviation, then recovery.
PERSISTENT
Abnormal behaviour continues.
Illustrative throughput sequence
92
t1
95
t2
91
t3
30
t4
93
t5
96
t6
94
t7
One sudden drop that recovers may be transient; a sustained drop may be persistent.

## Slide 3
02 • OBJECTIVES
What this project aims to do
Separate detection of abnormal behaviour from its duration-based interpretation.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
3
01
Prepare KPI time series
Handle timestamps, missing values, scaling and windows.
02
Learn normal behaviour
Train an LSTM Autoencoder mainly on baseline recordings.
03
Detect deviations
Use reconstruction error and a validation-derived threshold.
04
Interpret duration
Use temporal continuity to flag short-lived vs sustained anomalies.

## Slide 4
03 • DATASET
SpotLight Open RAN dataset
Experiments use baseline and anomaly recordings from the SpotLight project.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
4
BASELINE RECORDINGS
• 1UE • 5UE • 7UE-Ping
Used primarily to learn normal KPI patterns.
ANOMALY CATEGORIES
• MAC • MIXED • NETWORK • PDCP • RADIO
Used for testing and analysis.
Saved experiment split: 57 baseline recordings (40 train, 8 validation, 9 normal test) + 16 anomaly recordings.
12 selected KPI features • Source: SpotLight Open RAN dataset

## Slide 5
04 • METHODOLOGY
End-to-end system pipeline
The system first detects unusual windows, then examines continuity over time.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
5
KPI DATA
timestamped multivariate series
PREPROCESS
clean • scale select features
WINDOWS
20 time steps × 12 features
LSTM AE
learn normal patterns
ERROR
reconstruction MSE
DECISION
threshold + duration rules
NORMAL
TRANSIENT
PERSISTENT
Conceptual workflow; duration rules require validation against event-level ground truth.

## Slide 6
05 • MODEL
How the LSTM Autoencoder works
An encoder compresses the sequence; a decoder reconstructs it.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
6
INPUT
20 × 12 KPI window
ENCODER
LSTM 64 → 32
LATENT
compact sequence
DECODER
LSTM 32 → 64
OUTPUT
reconstructed 20 × 12
LOW RECONSTRUCTION ERROR
Sequence resembles learned normal behaviour.
HIGH RECONSTRUCTION ERROR
Sequence may be anomalous; compare with threshold.
Training objective: minimize mean squared reconstruction error (MSE).

## Slide 7
06 • DETECTION LOGIC
From reconstruction error to anomaly flag
Thresholding provides the first-stage decision.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
7
RECONSTRUCTION ERROR
MSE = average of (actual KPI − reconstructed KPI)²
THRESHOLD RULE
Error > threshold → Anomaly Error ≤ threshold → Normal
Saved run threshold: 0.028941 (reported as validation 95th percentile).
Important reproducibility note: the saved configuration also mentions a 99th percentile. This mismatch should be checked before claiming a final calibrated threshold.

## Slide 8
07 • EXPERIMENT
Model and training configuration
Values below are from the saved experiment artifacts.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
8
Input window
20 time steps × 12 features
Architecture
LSTM 64 → 32 → 32 → 64; Dense output
Loss / optimizer
Mean squared error / Adam
Learning rate
0.001
Batch size / epochs
64 / up to 100
Training data
Baseline KPI windows
Training loss decreased from approximately 0.30791 to 0.02193; minimum validation loss was approximately 0.00990.

## Slide 9
08 • RESULTS
Detection performance on the saved test run
Metrics show useful anomaly signal, but substantial false positives remain.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
9
Accuracy
68.32%
Precision
28.55%
Recall
58.10%
F1-score
38.29%
ROC–AUC
0.688
PR–AUC
0.356
Interpretation: recall is higher than precision, meaning many labelled anomalies are found, but many normal windows are also flagged.
These are saved-run results, not a claim of production-ready performance.

## Slide 10
09 • ERROR ANALYSIS
Confusion matrix: false alarms are a major issue
Window-level counts from the saved evaluation.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
10
TRUE NEGATIVES
101,371
FALSE POSITIVES
42,613
FALSE NEGATIVES
12,283
TRUE POSITIVES
17,031
Practical implication: threshold calibration, feature scaling, class imbalance and event-aware scoring need further investigation.

## Slide 11
10 • TRANSIENT VS PERSISTENT
Duration-based classification: current status
The project includes a duration rule, but this stage is not yet validated as a classifier.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
11
TRANSIENT
Anomaly appears briefly and returns toward normal.
PERSISTENT
Anomaly remains elevated across time and does not recover.
Saved duration-rule output: 335 transient and 1,384 persistent detections (rule setting: 3 consecutive anomalous windows). These are rule-based outputs, not ground-truth-validated class counts.
Caution: windows are 20 time steps long with stride 1, so adjacent windows overlap heavily. Counting windows as elapsed duration can exaggerate persistence. Event-level ground-truth validation is still needed.

## Slide 12
11 • EVENT-LEVEL EVALUATION
Event matching reveals a key limitation
A detector can flag many windows yet produce too many separate predicted events.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
12
Reference events
69
Predicted events
1,719
Matched events
67
Event precision
3.90%
Event recall
97.10%
Event F1
7.49%
Priority improvement: merge nearby positive windows into coherent events, tune thresholds, and evaluate detection delay.

## Slide 13
12 • TRAINING RESULTS
Training and validation loss
Actual training-history figure saved by the project pipeline.
WHAT THE GRAPH SHOWS
• Training loss fell from ≈0.30791 to ≈0.02193. • Minimum validation loss was ≈0.00990 near epoch 99. • This indicates the model learned to reconstruct the training sequences; it does not by itself prove strong anomaly classification.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
13

## Slide 14
13 • DETECTION EVIDENCE
Reconstruction-error distributions
Saved plots help explain how the threshold separates normal and anomalous windows.
Normal test error distribution
Anomaly test error distribution
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
14

## Slide 15
14 • TIME-SERIES BEHAVIOUR
Anomaly timeline
A time view is needed because the project focuses on transient versus persistent events.
Note: adjacent windows overlap (20 samples, stride 1); duration must be calculated from timestamps/event merging, not raw window counts alone.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
15

## Slide 16
15 • WIRELESS-NETWORK EVALUATION
Which communication metrics fit this dataset?
Evaluate the ML model in terms of network behaviour—but only report metrics supported by measurements.
AVAILABLE KPI FEATURES
• PUSCH count / average PUSCH count • Uplink PRB size, maximum and minimum • Uplink MCS, minimum and maximum • Uplink transport block size (TBS), min/max • UL transmission count These can support analysis of radio-resource use, modulation/coding behavior and uplink transmission activity.
METRICS: DIRECT VS DERIVED
Potentially derivable after checking units and sampling interval: • Data-rate / throughput estimate from transmitted bits or TBS over time • PRB/resource-use trends; MCS/TBS behavior Not directly measured in the selected 12 features: • Latency, goodput, BER, PER, EVM • Spectral efficiency and ergodic capacity (need suitable rate/bandwidth/channel measurements)
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
16

## Slide 17
16 • WIRELESS IMPACT
How to evaluate network impact responsibly
The current experiment evaluates anomaly detection; it does not yet measure end-to-end wireless QoS.
REPORT NOW (SUPPORTED)
• Detection: precision, recall, F1, ROC–AUC, PR–AUC • False-positive rate and false alarms • Reconstruction error and threshold • KPI patterns around detected events • Radio-side proxies: PRB, MCS, TBS, UL transmission activity
TO CLAIM NETWORK QOS GAINS
Collect or derive, with units and sampling interval: • Throughput / goodput (bit/s) • Spectral efficiency (bit/s/Hz) • Latency (ms), PER and BER • EVM (%) and channel-quality measures • Ergodic capacity only with channel/SNR assumptions or measurements Then compare normal vs anomaly periods and, ideally, baseline detector vs proposed model.
Do not present unmeasured BER, PER, EVM, latency or capacity as achieved results. They are recommended future evaluation metrics if the required data becomes available.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
17

## Slide 18
17 • FINAL INTERPRETATION
What we can conclude from the current experiment
The model detects abnormal KPI windows, but reducing false alarms and validating event duration remain key.
ROC–AUC
0.688
WINDOW F1
38.29%
EVENT RECALL
97.10%
Wireless-communication interpretation: the selected KPIs describe uplink scheduling/resource use and transmission behavior. The model can help surface unusual radio-side operating patterns. However, the present dataset and saved outputs do not establish improvements in throughput, spectral efficiency, latency, BER/PER, EVM or capacity. Those require additional measurements and a controlled comparison.
Recommended next step: align each anomaly with timestamped radio KPIs, compute only metrics with valid units, and compare event-level performance against a baseline detector.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
18

## Slide 19
18 • DISCUSSION
What the current prototype demonstrates—and what remains
A clear, honest summary strengthens the final presentation.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
19
WHAT WORKS
• End-to-end KPI preprocessing and windowing
• LSTM Autoencoder trained on baseline data
• Reconstruction-error anomaly scoring
• Initial window-level and event-level evaluation
NEXT STEPS
• Resolve 95th vs 99th percentile threshold mismatch
• Reduce false positives and improve event merging
• Correct duration logic for overlapping windows
• Validate transient/persistent labels with ground truth
• Compare with simple baselines; measure detection delay
Category coverage is incomplete in saved labelled subsets for MAC and NETWORK; zero positive windows are not definitive evidence of failure.

## Slide 20
19 • CONCLUSION
Key takeaways
The project is a working prototype and a foundation for more reliable Open RAN monitoring.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
20
An LSTM Autoencoder can learn temporal patterns in baseline Open RAN KPIs.
Reconstruction error provides an initial anomaly signal.
The saved test run achieved ROC–AUC 0.688, but precision and event-level F1 remain low.
Transient vs persistent classification needs duration-aware, ground-truth validation.
Final message: detect unusual behaviour, then establish whether it persists before prioritizing action.

## Slide 21
20 • REFERENCES
Research and project resources
Key sources supporting the dataset and model approach.
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
21
• Sun et al., “SpotLight: Accurate, Explainable and Efficient Anomaly Detection for Open RAN,” ACM MobiCom 2024. DOI: 10.1145/3636534.3649380
• Malhotra et al., “LSTM-based Encoder-Decoder for Multi-sensor Anomaly Detection,” 2016. arXiv:1607.00148
• Su et al., “Robust Anomaly Detection for Multivariate Time Series through Stochastic Recurrent Neural Network (OmniAnomaly),” KDD 2019.
• Xu et al., “Unsupervised Anomaly Detection via Variational Auto-Encoder for Seasonal KPIs in Web Applications (Donut),” 2018.
• SpotLight code repository: github.com/netsys-edinburgh/SpotLight

## Slide 22
FINAL PROJECT PRESENTATION
Thank you.
Questions & Discussion
LSTM Autoencoder-Based Persistent and Transient Anomaly Classification in Open RAN KPIs
Department of Electronics & Communication Engineering
LSTM AUTOENCODER • OPEN RAN KPI ANOMALY CLASSIFICATION
22